## Slide 1: CSCI 2400 Computer Systems
Spring 2017
Professor Rick Han
Department of Computer Science
University of Colorado at Boulder
rhan@cs.colorado.edu
http://www.cs.colorado.edu/~rhan

## Slide 2: Goal of 2400:
Learn how a computer works!
  More precisely, how software executes on modern computer hardware
Python,
Java,
C code
2400 Magic
More Magic!
App
.exe
Great Material but Challenging!
Notes: Computer Systems focuses primarily on understanding how a *single* program executes on a computer, though Chapter 8 starts to introduce the notion of multiple programs. To fully understand how a computer works, you really have to take Operating Systems, which explains with how a computer handles *multiple* programs executing on a computer.

## Slide 3: 2400 In a Nutshell
Python,
Java, C
code
Pre-processor
&
Compiler
Assembler
&
Linker
Lines of
Binary
code &
data
10101010
00001010
01010111
11101110
00111011
10000111
Memory
10101010
Lines of
Assembly
code
add a,b
sub a,b
move a…
Notes: This is simplified. There are actually more steps, like operating system (OS) interactions, I/O and more hardware, like a disk/flash for permanent storage, caching, etc.

## Slide 4: Chapter Mapping
Lines of
Source
code
Lines of
Assembly
code
Lines of
Binary
code &
data
10101010
00001010
01010111
Memory
11101110
00111011
10000111
10101010
add a,b
sub a,b
move a…
Chapter 3
Chapters 3, 4, 5 and 6
Chapter 7
Chapter 9
Chapter 5
Chapter 2
Pre-processor
&
Compiler
Assembler
&
Linker
Operating
System
Chapter 8
Notes: Not shown is Chapter 8, which covers how an executing program interfaces with the OS via system calls and exception handling.

## Slide 5: Approximate Timeline
Week | Topics | Due
1 | Ch 1-2: Intro, Two’s Complement | 
2 | Ch 2: Integer Arithmetic | 
3 | Ch 3: Assembly memory, arithmetic | Data Lab
4 | Ch 3: Assembly control flow, loops | 
5 | Ch 3: Assembly: stacks, arrays | 
6 | Ch 3: Assembly: structs, 64-bit | Bomb Lab
7 | Ch 2: Floating point | MT 1
8 | Ch 4: ISA, Pipelining | 
9 | Ch 4-5: Pipelining, Optimization | Attack Lab
10 | Ch 5: Performance Optimization | 
11 | Ch 6: Caching | Performance Lab
12 | Ch 6: Caching, Storage | MT 2
13 | Ch 8: Exceptions, Signals | 
14 | Ch 9: Virtual Memory | Shell Lab
15 | Ch 7: Linking | 
Finals | Final Exam | Final Exam

## Slide 6: Announcements
Let’s go to moodle.cs.colorado.edu, the primary rendezvous point for CS 2400
  Sign up for an account, using ‘2400rocks2017’ as the enrollment key
  Walk through the syllabus

## Slide 7: Announcements
C Assessment quiz due Friday by 12 pm noon
  Go to the moodle and do the C Assessment quiz by the deadline this week
  Make sure you understand C pointers
  Suggested C refresher tutorial/study links:
    http://www.tutorialspoint.com/cprogramming/
    http://learn-c.org/
  Unlimited # of attempts
  If your score <= 70%, you need to attend Friday’s C tutorial
  More announcements on this quiz will be made on the moodle

## Slide 8: Announcements
First data lab to be released on moodle, due in ~3 weeks
First recitation with TAs this week
  Install the 2400 class VM (VirtualBox-based) on your laptops
  Introduce data lab
  Bit manipulation operations
Read Chapter 1 and 2.1-2.3 (skip floating point)

## Slide 9: Hints!
  Do not fall behind on the reading in this class!
  Do all practice problems in the textbook! (solutions are there)
  Attend lectures!
  Skip roadblocks and circle back
Notes: Especially through Chapter 3, you cannot afford to skip readings for even a week!
Don’t worry if you don’t understand a sentence or paragraph. Move forward to the next paragraph, circle back, ask the TA, CA and prof Qs.

## Slide 10: Systems as a Springboard…
CS 2270
Fundamental
Structures
CS 2400
Systems
CS 3753
Operating
Systems
CS 3155
Programming Lang
Processes
Mem. Mgmt
Machine Code
Optimization
Data Structures
Applications
Programming
CS 4273
Networks
Network
Protocols
ECE 347
Architecture
CSCI 3656
Numerical Comp
Exec. Model
Memory System
CS 1300
Programming

## Slide 11: Why C?
A good compromise between a high-level programming language and low-level hardware
  Maps well to assembly and binary machine code instructions
  Low level enough to manipulate memory with pointers
    Learn from C about the dangers of pointer arithmetic, array out-of-bounds memory accesses, etc. – we’ll study some of these
Most operating systems and network protocol stacks are built with C, as are many high-performance applications

## Slide 12: 2400 In a Nutshell
Python,
Java, C
code
Pre-processor
&
Compiler
Assembler
&
Linker
Lines of
Binary
code &
data
10101010
00001010
01010111
11101110
00111011
10000111
Memory
10101010
Lines of
Assembly
code
add a,b
sub a,b
move a…
Notes: This is simplified. There are actually more steps, like operating system (OS) interactions, I/O and more hardware, like a disk/flash for permanent storage, caching, etc.

## Slide 13: Hardware Organization of a Computer System (Von Neumann)
General Architecture
load
Lines of
Binary
code &
data
10101010
00001010
01010111
11101110
00111011
10000111
Notes: This architecture enabled *progammable computing*, which was a huge improvement over mechanical computers with relays, which could typically only run one program ever, or were very difficult to reprogram.
Also there's a Harvard architecture for computers, which has separate memories and buses for instructions and data. It's used in embedded microcontrollers and DSPs for speed because both data and instructions can be fetched in parallel, unlike pure Von Neumann architectures. The Harvard separation of instructions and data is often used in today's CPU caches, though not necessarily for main memory.

## Slide 14: Hardware Organization of a Computer System
General Architecture
Lines of
Binary
code &
data
10101010
00001010
01010111
11101110
00111011
10000111

## Slide 15: Hardware Organization of a Computer System
General Architecture
store
Lines of
Binary
code &
data
10101010
00001010
01010111
11101110
00111011
10000111

## Slide 16: Inside the CPU - Building Blocks
Registers
  Data (16 in IA64)
  Instruction register (IR) = current instruction
  Program counter (PC) = pointer to next instruction in memory
Control Unit (not shown)
  Communicate with RAM
Data registers
RAM

## Slide 17: Arithmetic Logic Unit (ALU) of CPU
Performs two types of operations
  Arithmetic: ADD, SUBTRACT, etc.
  Logic: AND, OR, NOT, XOR, >, <
In the picture,
  A and B are the input data or operands
  F = function to perform, i.e. +, -, AND, XOR, etc.
  R = result
  D = any flags due to operation, such as a carry, overflow, sign, etc.
A, B, and R are all stored in registers
  As we will see, one type of instruction moves instructions and data to/from CPU from/to memory
    i.e. fetch A and B from memory, move R to memory
  Another type of instruction uses ALU to operate on this data

## Slide 18: Layout of a Program in Memory
Program memory is divided into 4 sections
  Code
  Data
  Heap
  Stack
Stack grows down from high memory by convention on IA32
Heap grows up from low memory by convention
MAX
Notes:   This is actually virtual memory, not physical memory. The Stack stores local variables and supports function calls. The Heap supports dynamic run-time memory allocation like malloc(). Arguably, memory-mapped libraries constitute a 5th “region” of virtual memory.

## Slide 19: Cache For Faster Data/Code Access
Lines of
Binary
code &
data
10101010
00001010
01010111
11101110
00111011
10000111
Slow
Fast
Cache

## Slide 20: Cache For Faster Data/Code Access
Caching
  Going to memory is quite slow compared to the speed of the CPU
    RAM access time is ~ microseconds.
    CPU executes multiple instructions per nanosecond.
    So CPU waits ~1000 cycles to fetch data from memory!
  Solution: create a smaller but faster buffer called a cache, and cache data there that is going to be used soon
    In reality, cache data that was more recently used
  Why not cache all data in registers?
    Too expensive/byte

## Slide 21: Memory Hierarchy

## Slide 22: Memory Hierarchy
Intel Core i7 organization
  4 cores
  Each core has an L1 data cache, an L1 instruction cache, and a larger but slower L2 unified cache
  Across cores, there is an L3 unified cache

## Slide 23: Pipelining to Improve Throughput
Pipelining
  Instructions can be broken up into stages.
  Design CPU with multiple stages or “pipeline”.
  As a stage finishes, it accepts the result from the previous stage -> Faster!
  Sequential non-pipelined is slower, some stages empty.