## Slide 1: Chapter 2: Bits and Bytes
Topics
  Why bits?
  Binary Logic
  Representing information as bits
    Binary/Hexadecimal
    Byte representations
      ints, floats, double precision

## Slide 2: Recap: Systems In a Nutshell
Lines of
Source
code
Lines of
Assembly
code
Lines of
Binary
code &
data
10101010
00001010
01010111
Memory
11101110
00111011
10000111
10101010
add a,b
sub a,b
move a…
Chapter 2
Pre-processor
&
Compiler
Assembler
&
Linker

## Slide 3: Decimal Representation
Decimal representation (Base 10) is what we humans naturally gravitate to, given 10 digits (fingers)!
  7126 base 10 = 712610
  = 7000 + 100 + 20 + 6
  = 7*103 + 1*102 + 2*101 + 6*100
  By convention, we write the most significant digit on the left, followed by the second most significant digit, then the 3rd most significant digit, etc., until we reach the least significant digit

## Slide 4: Binary Representation – Why Bits?
0 1 0 12 = 0*23 + 1*22 + 0*21 + 1*20
= 0 + 4 + 0 + 1 = 510
Each binary digit is called a ‘bit’
Base 2 or Binary is easier to represent via electronic circuits than Base 10
  Digital transistor circuits can easily represent a ‘0’ and a ‘1’
    A ‘1’ = +5 volts, a ‘0’ = 0 volts, so only 2 voltage levels
    Don’t have to implement 10 different voltage levels as in base 10
  Easy to implement Base 2 arithmetic
    much of Base 10 arithmetic using Base 2 arithmetic (integers are exact, but floats are approximations)
  Easy to implement digital logic (AND, OR, etc.) with binary
Notes:     Most digital circuits today are based on CMOS (Complementary Metal Oxide Semiconductor) technology.
    CMOS typically combines together NMOS and PMOS transistors to form digital logic and arithmetic circuits

## Slide 5: Digital Logic via Boolean Algebra
Developed by George Boole in 19th Century
  Algebraic representation of logic
    Encode “True” as 1 and “False” as 0
And “&”
  A&B = 1 only when both A=1 and B=1
A
B
A | B | &
0 | 0 | 0
1 | 0 | 0
0 | 1 | 0
1 | 1 | 1
Truth Tables
(two forms)
Notes: Now we’re representing variables as TRUE/FALSE Booleans *and* performing *logical* operations on them. In the next subsections, we’ll consider representing variables as integers, and performing *arithmetic* operations on them. Note the above tables are called “truth tables”.

## Slide 6: Common Digital Logic Operations
Not “~”
  ~A = 1 only when A=0
Or “|”
  A|B = 1 when either A=1 or B=1
Exclusive-Or (Xor) “^”
  A^B = 1 when either A=1 or B=1, but not both
And “&”
  A&B = 1 only when both A=1 and B=1
A
B
Other operators: NAND (Not AND), NOR (Not OR), etc.
Notes: Now we’re representing variables as TRUE/FALSE Booleans *and* performing *logical* operations on them. In the next subsections, we’ll consider representing variables as integers, and performing *arithmetic* operations on them. Note the above tables are called “truth tables”.