## Slide 1: Chapter 2: Bits and Bytes
Topics
  Why bits?
  Binary Logic
  Representing information as bits
    Binary/Hexadecimal
    Byte representations
      ints, floats, double precision

## Slide 2: Announcements
Moodle is having difficulty emailing announcements
Data Lab is due Friday Feb 3 by 11:55 pm
  Bit manipulation operations
C assessment quiz due Friday Jan 20 by noon
  Unlimited # of attempts
  If you score <=70%, then attend C tutorial Friday evening (TA Yogesh will announce)
Chap 2 Data Quiz is due Monday Jan 30 by noon
  Addition, subtraction, signed, overflow
Read Chapter 2.1-2.3 and do practice problems

## Slide 3: Recap: Systems In a Nutshell
Lines of
Source
code
Lines of
Assembly
code
Lines of
Binary
code &
data
10101010
00001010
01010111
Memory
11101110
00111011
10000111
10101010
add a,b
sub a,b
move a…
Chapter 2
Pre-processor
&
Compiler
Assembler
&
Linker

## Slide 4: Binary Representation – Why Bits?
0 1 0 12 = 0*23 + 1*22 + 0*21 + 1*20
= 0 + 4 + 0 + 1 = 510
Each binary digit is called a ‘bit’
Base 2 or Binary is easier to represent via electronic circuits than Base 10
  Digital transistor circuits can easily represent a ‘0’ and a ‘1’
    A ‘1’ = +5 volts, a ‘0’ = 0 volts, so only 2 voltage levels
    Don’t have to implement 10 different voltage levels as in base 10
  Easy to implement Base 2 arithmetic
    much of Base 10 arithmetic using Base 2 arithmetic (integers are exact, but floats are approximations)
  Easy to implement digital logic (AND, OR, etc.) with binary
Notes:     Most digital circuits today are based on CMOS (Complementary Metal Oxide Semiconductor) technology.
    CMOS typically combines together NMOS and PMOS transistors to form digital logic and arithmetic circuits

## Slide 5: Common Digital Logic Operations
Not “~”
  ~A = 1 only when A=0
Or “|”
  A|B = 1 when either A=1 or B=1
Exclusive-Or (Xor) “^”
  A^B = 1 when either A=1 or B=1, but not both
And “&”
  A&B = 1 only when both A=1 and B=1
A
B
Other operators: NAND (Not AND), NOR (Not OR), etc.
Notes: Now we’re representing variables as TRUE/FALSE Booleans *and* performing *logical* operations on them. In the next subsections, we’ll consider representing variables as integers, and performing *arithmetic* operations on them. Note the above tables are called “truth tables”.

## Slide 6: Implementing Digital Logic
Silicon transistor (NMOS)
  Three terminals. Input is the Gate G
  Acts like a simple ON/OFF switch
  Current flows from high voltage to low voltage
G
D
S
G = High
voltage
Current
can flow
  When a high voltage is applied to the input Gate G, then this connects the two terminals D and S, i.e. closes the switch, and current flows between them
D
S
G = Low
voltage
No
Current
flows
  When a low voltage is applied to Gate, then the two terminals are disconnected, i.e. opens the switch, and no current flows
D
S
Notes: This is an example of an n-type Metal Oxide Semiconductor (MOS) Field Effect Transistor (FET), or NMOS for short. See MOSFET for more.

## Slide 7: Implementing an Inverter or Not “~” Operation
  Thus we have an inverter or Not “~” operator:
    Input ‘1’ (High voltage) => output ‘0’ (Low voltage)
    Input ‘0’ (Low voltage) => output ‘1’ (High voltage)
Input = High
Output
= Low
Power
Ground
resistor
R
Input = Low
Output
= High
Power
Ground
resistor
R
Low input means no current flows, so output stay high
Voltage drop when current flows
Input
Output
Power = +3 or +5 Volts
Ground
= 0 Volts
resistor
R
An Inverter circuit
High input connects Output to Ground
Notes: See Wikipedia for more.

## Slide 8: Implementing a NAND operation
How do I make an AND gate?
  Concatenate an inverter after a NAND gate!
  AND gate symbol:
NAND = Negative AND
  Output = ~(A AND B)
Power
Ground
Pmos transistor
has opposite
behavior of nmos
NAND
A
B
  Symbol for a NAND gate is:
Notes: Top two transistors are pmos, while the bottom two transistors are nmos. Pmos has the opposite behavior of nmos, namely when the input to a pmos transistor is HIGH, then two terminals are disconnected, while when the input is LOW, the two terminals are connected. Mixing nmos and pmos transistors creates Complementary MOS (CMOS) digital logic circuits.

## Slide 9: Binary Digital Logic Symbols
Notes: See Wikipedia for more.

## Slide 10: Building a Binary Adder
One-bit Half Adder circuit
  Sum bit S = A XOR B
  Carry bit C = A AND B
One-bit Full Adder circuit extends Half Adder to also account for a bit carried in, not just the bit carried out
Example: an 8-bit Full Adder can be built by concatenating 8 one-bit Full Adders
Bit A | Bit B | Sum S | Carry C
0 | 0 | 0 | 0
0 | 1 | 1 | 0
1 | 0 | 1 | 0
1 | 1 | 0 | 1
One-bit Half Adder Circuit
Notes: See Wikipedia for more.

## Slide 11: Binary Representation (2)
Base 2 vs. Decimal conversion example:
  89 base 10 = 8910 = what in base 2 or binary?
  Find the largest power of 2 that is <= # and then subtract.
  Keep iterating until #=0.
  8910 = 64 + 16 + 8 + 1
  = 26 + 24 + 23 + 20
  = 0*27 + 1*26 + 0*25 + 1*24 + 1*23 + 0*22 + 0*21 + 1*20
  = 0 1 0 1 1 0 0 1 2
Notes: Other conversion methods: count how many times you can divide the number by 2 until the result is less than one, let count = count – 1, then remember this bit as 1*2^count. Let number = number – 1*2^count. Reset count = 0. Repeat until number is <=1.

## Slide 12: Hexadecimal Representation
Hexadecimal (base 16) is more convenient (it’s power of 2) and compact notation for larger binary #’s
  Consider a 32-bit number:
  101011100011001010001010000110012
  This is hard to read. So form 4-bit groups.
  = 1010 1110 0011 0010 1000 1010 0001 10012
  We then use hexadecimal notation:
  Use characters ‘0’ to ‘9’ and ‘A’ to ‘F’
  = A E 3 2 8 A 1 9 16
  = 0xAE328A19
  “0x” signifies hexadecimal or just hex. Note lower case 0xae328a19 is also valid.
0
0
0000
1
1
0001
2
2
0010
3
3
0011
4
4
0100
5
5
0101
6
6
0110
7
7
0111
8
8
1000
9
9
1001
A
10
1010
B
11
1011
C
12
1100
D
13
1101
E
14
1110
F
15
1111
Hex
Decimal
Binary
Notes: 64 bits is the standard word size in IA64 architectures.

## Slide 13: How We Use These Representations
Since these are just numbers, we can use them to describe anything with numerical value
We’ll use them to describe the numerical values of data stored at various memory locations
  Different data values, like real and integer values, positive and negative
We’ll also use them to describe the addresses of memory locations
Later, our code instructions will be encoded in binary as well

## Slide 14: Byte-Addressed Memory
Byte = 8 bits
  Binary 000000002 to 111111112
  Decimal: 010 to 25510
  Hexadecimal 0016 to FF16
Memory Address
010
110
210
310
1410
1510
.
.
.
.
.
.
.
byte 0
byte 1
byte 2
byte 14
byte 15
8 bits
MEMORY
  Memory addresses are referenced by their byte number
    Example: a 16 byte memory
    Memory address 1510
    = 16th byte (since memory starts at 0)
    = binary address
    000000000000000000000000000011112 in bytes
    = hex address 0x0000000F in bytes
    This memory stores how many bits?
    Answer: 8*16 = 128 bits!
Notes: What we’re trying to bring out here is that binary, hex and decimal can be used to describe both the data values/bytes stored *in* memory as well as the addresses *of* the memory.

## Slide 15: Machine Words
Each CPU Has “Word Size”
  Nominal size of integer-valued data
    Including addresses
  Early microprocessors were 8-bit CPUs. Today, many embedded microcontrollers are still 8-bit.
  Intel evolved to 16-bit processors, and called these “words”.
    addw and movw are assembly instructions where the “w” suffix stands for a 16-bit word and implies that 16-bit values are being added or moved
  Most machines became 32 bits (4 bytes)
    addl and movl are assembly instructions where the “l” suffix stands for a “long word” and implies that 32-bit values are being added or moved
    Limits addresses to 4GB
    Becoming too small for memory-intensive applications

## Slide 16: Machine Words
Each CPU Has “Word Size”
  Most newer systems are 64 bits (8 bytes)
    Potentially address  1.8 X 1019 bytes or 18 Exabytes
    addq and movq are assembly instructions where the “q” suffix stands for “quad word” (4*16=64) and implies that 64-bit values are being added or moved
  Machines support multiple data formats
    Fractions or multiples of word size
    Always integral number of bytes

## Slide 17: Word-Oriented Memory Organization
Addresses Specify Byte Locations
  Address of first byte in word
  Addresses of successive words differ by 4 (32-bit) or 8 (64-bit)
0015
0014
0013
0012
0011
0010
0009
0008
0007
0006
0005
0004
32-bit
Words
Memory
(bytes)
Addr.
0003
0002
0001
0000
64-bit
Words
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
0012
0008
0004
0000
0008
0000

## Slide 18: Data Representations
Sizes of C Objects (in Bytes)
  C Data Type Intel_x64 Typical 32-bit Intel IA32
    int 4 4 4
    long int 8 4 4
    char 1 1 1
    short 2 2 2
    float 4 4 4
    double 8 8 8
    long double 10/16 8 10/12
    char * 8 4 4
      Or any other pointer
    A float is a real # like -2.7143*10(-3). A double just provides more precision than a float, something like 2.71433273882*10(-3)
    A pointer stores an integer–like value that is interpreted as a memory location/address

## Slide 19: Storing Data in Memory
IA32 Example:
  Address of int is 0x00000000
  Address of float is 0x00000004
  Address of character = ‘7’ is 0x00000009
  Address of pointer is 0x0000000c
    Note: the pointer points to another memory location, i.e. stores a memory location address
‘x’
‘y’
‘7’
‘!’
0015
0014
0013
0012
0011
0010
0009
0008
0007
0006
0005
0004
Memory
(bytes)
Addr.
0003
0002
0001
0000
int
4 bytes
float
4 bytes
char 1 byte
char 1 byte
char 1 byte
char 1 byte
pointer
4 bytes
value
value
    e.g. if pointer = 0x00000004 it means the pointer is pointing to the float! (actually the first byte of the float)
value=
address

## Slide 20: Pointers in C
To declare a pointer to say an integer, here’s some code:
  int x;
  int *p = &x;
  int * p declares the variable p to be a pointer to an integer
  note how it differs from the declaration ‘int p’, which would just declare p to be an integer, not a pointer to an integer
  &x means find the memory location/address of x
  Thus, int *p = &x means initialize the value of the pointer p with the address of integer variable x.

## Slide 21: Dereferencing Pointers in C
To find the value of a variable being pointed to, you must dereference a pointer. Here’s some code:
  int x;
  int *p = &x;
  int y = *p;
  p is a pointer to an integer. To get the value of the integer that p is pointing to, you use the dereference operator (*).
  note how * is used first to declare a pointer, and is used later to dereference a pointer to find the value of the variable it is pointing to
  Here, y = x.

## Slide 22: Pointer Values
Since the pointer value is an address, then it doesn’t matter what type of variable is being pointed to, the size of the pointer value is always 4 bytes (IA32)
  char c;
  int x;
  double d;
  char *p1 = &c;
  int *p2 = &x;
  double *p3 = &d;
  p1 is a pointer to a one-byte long char, but is 4 bytes long, because the address of the char is 4 bytes long.
  p3 is a pointer to an 8-byte long double, but is 4 bytes long, because the address of the double (lowest byte) is 4 bytes long.

## Slide 23: Relations Between Logic Operations
DeMorgan’s Laws
  Express & in terms of |, and vice-versa
    A & B = ~(~A | ~B)
      A and B are true if and only if neither A nor B is false
    A | B = ~(~A & ~B)
      A or B are true if and only if A and B are not both false
Exclusive-Or using Inclusive Or
    A ^ B = (~A & B) | (A & ~B)
      Exactly one of A and B is true
      This is Shannon’s circuit.
    A ^ B = (A | B) & ~(A & B)
      Either A is true, or B is true, but not both

## Slide 24: General Boolean Algebras
Operate on Bit Vectors
  Operations applied bitwise
All of the Properties of Boolean Algebra Apply
01101001
& 01010101
01000001
01101001
| 01010101
01111101
01101001
^ 01010101
00111100
~ 01010101
10101010
01000001
01111101
00111100
10101010
Notes: For logical operations, the bitwise AND, OR, XOR, etc. is self-contained independently within each bit column, i.e. there is no such thing as a carry from one column to the next.

## Slide 25: Using Boolean Operators for Representing & Manipulating Sets
Representation
  Width w bit vector represents subsets of {0, …, w–1}
  aj = 1 if j  A
    01101001 { 0, 3, 5, 6 }
    76543210
    01010101 { 0, 2, 4, 6 }
    76543210
Operations
  & Intersection 01000001 { 0, 6 }
  | Union 01111101 { 0, 2, 3, 4, 5, 6 }
  ^ Symmetric difference 00111100 { 2, 3, 4, 5 }
  ~ Complement 10101010 { 1, 3, 5, 7 }

## Slide 26: Bit-Level Operations in C
Operations &, |, ~, ^ Available in C
  Apply to any “integral” data type
    long, int, short, char
  View arguments as bit vectors
  Arguments applied bit-wise
Examples (Char data type)
  ~0x41 --> 0xBE
    ~010000012 --> 101111102
  ~0x00 --> 0xFF
    ~000000002 --> 111111112
  0x69 & 0x55 --> 0x41
    011010012 & 010101012 --> 010000012
  0x69 | 0x55 --> 0x7D
    011010012 | 010101012 --> 011111012

## Slide 27: Supplementary Slides

## Slide 28: Integer Algebra vs. Boolean Algebra
Integer Arithmetic
  Z, +, *, –, 0, 1 forms a “ring”
  Addition is “sum” operation
  Multiplication is “product” operation
  – is additive inverse
  0 is identity for sum
  1 is identity for product
Boolean Algebra
  {0,1}, |, &, ~, 0, 1 forms a “Boolean algebra”
  OR is “sum” operation
  AND is “product” operation
  ~ is “complement” operation (not additive inverse)
  0 is identity for sum
  1 is identity for product

## Slide 29
  Commutativity
  A | B = B | A A + B = B + A
  A & B = B & A A * B = B * A
  Associativity
  (A | B) | C = A | (B | C) (A + B) + C = A + (B + C)
  (A & B) & C = A & (B & C) (A * B) * C = A * (B * C)
  Product distributes over sum
  A & (B | C) = (A & B) | (A & C) A * (B + C) = A * B + A * C
  Sum and product identities
  A | 0 = A A + 0 = A
  A & 1 = A A * 1 = A
  Zero is product annihilator
  A & 0 = 0 A * 0 = 0
  Cancellation of negation
  ~ (~ A) = A – (– A) = A
Boolean Algebra  Integer Ring

## Slide 30
  Boolean: Sum distributes over product
  A | (B & C) = (A | B) & (A | C) A + (B * C)  (A + B) * (A + C)
  Boolean: Idempotency
  A | A = A A + A  A
    “A is true” or “A is true” = “A is true”
  A & A = A A * A  A
  Boolean: Absorption
  A | (A & B) = A A + (A * B)  A
    “A is true” or “A is true and B is true” = “A is true”
  A & (A | B) = A A * (A + B)  A
  Boolean: Laws of Complements
  A | ~A = 1 A + –A  1
    “A is true” or “A is false”
  Ring: Every element has additive inverse
  A | ~A  0 A + –A = 0
Boolean Algebra  Integer Ring

## Slide 31: Properties of & and ^
Boolean Ring
  {0,1}, ^, &, , 0, 1
  Identical to integers mod 2
   is identity operation:  (A) = A
    A ^ A = 0
Property Boolean Ring
  Commutative sum A ^ B = B ^ A
  Commutative product A & B = B & A
  Associative sum (A ^ B) ^ C = A ^ (B ^ C)
  Associative product (A & B) & C = A & (B & C)
  Prod. over sum A & (B ^ C) = (A & B) ^ (A & C)
  0 is sum identity A ^ 0 = A
  1 is prod. identity A & 1 = A
  0 is product annihilator A & 0 = 0
  Additive inverse A ^ A = 0

## Slide 32: Application of Boolean Algebra
A
~A
~B
B
Connection when
A&~B | ~A&B
Applied to Digital Systems by Claude Shannon
  1937 MIT Master’s Thesis
  Reason about networks of relay switches
    Encode closed switch as 1, open switch as 0
A&~B
~A&B
= A^B

## Slide 33: Binary Digital Logic Circuit Example
CMOS inverter circuit
  Vdd = Power = +3 Volts, Vss = Ground = 0 Volts
  Current flows from high voltage to low voltage
  When input A = 0 V (Ground), then nmos transistor is shut off, while the pmos transistor is turned on, so Q is connected to Vdd = +3 V
pmos
nmos
= 0 V
~= +3 V
= +3 V
= 0 V
pmos
nmos
= 3 V
~= 0 V
= +3 V
= 0 V
  When input A = +3 V (Power), then pmos is off and nmos is on, so Q is connected to ground and is pulled down to 0 V
  So Q is the opposite or inverse of A!
  i.e. Q = ~A
  AND, OR, NAND, NOR, ADD, SUBTRACT, etc. are also implemented this way…
Notes: See Wikipedia for more.

## Slide 34: Byte-Oriented Memory Organization
Programs Refer to Virtual Addresses
  Conceptually very large array of bytes
  Actually implemented with hierarchy of different memory types
    SRAM, DRAM, disk
    Only allocate for regions actually used by program
  Address space private to particular “process”
    Program being executed
    Program can clobber its own data, but not that of others
Compiler + Run-Time System Control Allocation
  Where different program objects should be stored
  Multiple mechanisms: static, stack, and heap
  In any case, all allocation within single virtual address space