## Slide 1: Chapter 2: Integer Arithmetic and Overflow
  Casting between signed and unsigned integers
  Sign extension
  Integer multiplication
  Integer division

## Slide 2: Announcements
Chap 2 Data Quiz is due Monday Jan 30 by noon
  Addition, subtraction, signed, overflow
Data Lab is due Friday Feb 3 by 11:55 pm
  Bit manipulation operations
Assigned new TA: Rohit Gupta
In the process of creating a new recitation Wednesday 4 pm – stay tuned for more details
Read Chapter 2.1-2.3 and do practice problems

## Slide 3: Recap…
Bit masking using the “&” operator
Logical operators “&&”, “||” and “!”
Bit shifting
  Left shifting “<<“ = multiplication by a power of two
  Right shifting “>>” = division by a power of two
    Logical
    Arithmetic
Unsigned binary encoding
  Unsigned modular addition
  overflow
Signed two’s complement binary encoding
  Signed modular addition
  Positive and negative overflow regions

## Slide 4: Summarizing…
TAdd4(u , v)
u
v
PosOver
NegOver
Two’s complement Overflow
  Two large positive #’s can sum to a negative # (PosOver)
    Then, sum of u and v = TrueSum(u + v) - 2w, given w bits
  Two large negative #’s can sum to a positive # (NegOver)
    Then, sum of u and v = TrueSum(u + v) + 2w, given w bits

## Slide 5: Checking for Signed Overflow in C
Approach #1
  Have the compiler insert checks every time a signed integer arithmetic operation is performed
  Use gcc compiler with –ftrapv flag
Approach #2
  Manually insert the checks yourself
  Can use macros, e.g. replace each add ‘+’ with a macro ADD(A,B)
    These macros essentially test the operands against the integer limits in the header file <limits.h> before doing the operation
  See CERT Web page for examples
    https://www.securecoding.cert.org/confluence/display/seccode/INT32-C.+Ensure+that+operations+on+signed+integers+do+not+result+in+overflow?showComments=false
  Some compiler optimization may remove these code checks
Approach #3 : ignore and hope = risky strategy
Notes: In Approach #1, the –ftrapv flag will cause a SIGABRT signal to be sent to the application that caused the overflow. To see a message that this was an overflow, add a signal handler for SIGABRT to your code, and inside it print “Overflow occurred”. We’ll cover signals later in the course.

## Slide 6: Unsigned & Signed Numeric Values
Equivalence
  Same encodings for nonnegative values
Uniqueness
  Every bit pattern represents unique integer value
  Each representable integer has unique bit encoding
 Can Invert Mappings
  U2B(x) = B2U-1(x)
    Bit pattern for unsigned integer
  T2B(x) = B2T-1(x)
    Bit pattern for two’s comp integer
X
B2T(X)
B2U(X)
0000
0
0001
1
0010
2
0011
3
0100
4
0101
5
0110
6
0111
7
–8
8
–7
9
–6
10
–5
11
–4
12
–3
13
–2
14
–1
15
1000
1001
1010
1011
1100
1101
1110
1111
0
1
2
3
4
5
6
7
Notes: Note: if you’re given just a set of N bits and told they represent an integer number, one cannot tell if those bits should be interpreted as an unsigned integer or a two’s complement (or other encoding) signed integer. You can infer which it is based on the context in which that number is used, e.g. if it is used in an assembly language instruction that performs signed addition, then you know it is likely meant to be a two’s complement binary representation.
B2T^-1 can be done as follows: given a signed integer X, determine first if its sign is + ‘0’ or – ‘1’. (A) If +, then use the same approach as inverting U2B, i.e. B2U^-1, set current value V = X and find the largest power y of 2<= V, i.e. 2^y <= V, remember this bit position, then subtract 2^y from V, and keep iterating until done. (B) If -, for a w-bit encoding, then set current value V = X, then add 2^(w-1) to V and remember the MSbit =1. With this new V, work out the binary encoding as in (A).

## Slide 7: Casting Signed to Unsigned
short int x = 15213;
unsigned short int ux = (unsigned short) x;
short int y = -15213;
unsigned short int uy = (unsigned short) y;
C Allows Conversions from Signed to Unsigned
Resulting Value
  No change in bit representation
  Nonnegative values unchanged
    ux = 15213
  Negative values change into (large) positive values
    uy = 50323
  Because conversion between signed and unsigned is so confusing, languages like Java only permit signed integers

## Slide 8: Relation between Signed & Unsigned
T2U
T2B
B2U
Two’s Complement
Unsigned
Maintain Same Bit Pattern
y
uy
Y
+
+
+
+
+
+
• • •
-
+
+
+
+
+
• • •
uy
y
-
w–1
0
+2w–1 – –2w–1 = 2*2w–1 = 2w
-15213
50323

## Slide 9: Relation Between Signed & Unsigned
  uy = y + 2 * 215 = y + 2* 32768 = y + 65536 (y<0)

## Slide 10: Signed vs. Unsigned in C
Constants
  By default are considered to be signed integers
  Unsigned if have “U” as suffix
    0U, 4294967259U
Casting
  Explicit casting between signed & unsigned same as U2T and T2U
    int tx, ty;
    unsigned int ux, uy;
    tx = (int) ux;
    uy = (unsigned) ty;
  Implicit casting also occurs via assignments and procedure calls
    tx = ux;
    uy = ty;

## Slide 11: Casting Surprises
  0 0U == unsigned
  -1 0 < signed
  -1 0U > unsigned
  2147483647 -2147483648 > signed
  2147483647U -2147483648 < unsigned
  -1 -2 > signed
  (unsigned) -1 -2 > unsigned
  2147483647 2147483648U < unsigned
  2147483647 (int) 2147483648U > signed
Expression Evaluation
  If mix unsigned and signed in single expression, signed values implicitly cast to unsigned
  Including comparison operations <, >, ==, <=, >=
  Examples for W = 32
Constant1 Constant2 Relation Evaluation
  0 0U
  -1 0
  -1 0U
  2147483647 -2147483648
  2147483647U -2147483648
  -1 -2
  (unsigned) -1 -2
  2147483647 2147483648U
  2147483647 (int) 2147483648U
Notes: 2^31 = 2147483648.

## Slide 12: Explanation of Casting Surprises
0
TMax
TMin
–1
–2
0
UMax
UMax – 1
TMax
TMax + 1
2’s Comp.
Range
Unsigned
Range
2’s Comp.  Unsigned
  Ordering Inversion
  Negative  Big Positive

## Slide 13: Sign Extension
Task:
  Given w-bit signed integer x
  Convert it to w+k-bit integer with same value
Rule:
  Make k copies of sign bit:
  X  = xw–1 ,…, xw–1 , xw–1 , xw–2 ,…, x0
k copies of MSB
• • •
X
X 
• • •
• • •
• • •
w
w
k

## Slide 14: Sign Extension Example
  Converting from smaller to larger integer data type
  C automatically performs sign extension
short int x = 15213;
int ix = (int) x;
short int y = -15213;
int iy = (int) y;
Decimal
Hex
Binary
x
15213
3B 6D
00111011 01101101
ix
15213
00 00 3B 6D
00000000 00000000 00111011 01101101
y
-15213
C4 93
11000100 10010011
iy
-15213
FF FF C4 93
11111111 11111111 11000100 10010011
Notes: In these examples, we have allocated enough memory so we can safely extend the *value* of say the 16 bit short into a 32-bit int’s memory space.

## Slide 15: Justification For Sign Extension
Prove Correctness by Induction on k
  Induction Step: extending by single bit maintains value
  Key observation: –2w–1 = –2w +2w–1
  Look at weight of upper bits:
    X –2w–1 xw–1
    X  –2w xw–1 + 2w–1 xw–1 = –2w–1 xw–1
-
• • •
X
X 
-
+
• • •
w+1
w

## Slide 16: Why Should I Use Unsigned?
Do Use in Limited Cases…
  When representing a set of Boolean flags with bits
  When representing addresses (IP or memory, always >=0)
  When performing modular & multiprecision arithmetic, etc.
Do Use When Need Extra Bit’s Worth of Range
  Working right up to limit of word size
Don’t Use Just Because Number Nonzero
  Easy to make mistakes
    unsigned int i;
    for (i = cnt-2; i > -1; i--)
    a[i] += a[i+1];
Loop not executed
when cnt is a large (+) #
  C compilers on some machines generate less efficient code
    unsigned int i;
    for (i = 1; i < cnt; i++)
    a[i] += a[i-1];
Loop executed
when cnt<0
Notes: In the second example, cnt could be a negative signed int, so for loop should not be executed. But, the negative value gets converted to a positive value when comparing unsigned I < signed cnt, so for loop is executed.
IP = Internet Protocol, i.e. network addresses.

## Slide 17: Multiplication
Computing Exact Product of w-bit numbers x, y
  Either signed or unsigned
Ranges
  Unsigned: 0 ≤ x * y ≤ (2w – 1) 2 = 22w – 2w+1 + 1
    Up to 2w bits
  Two’s complement min: x * y ≥ (–2w–1)*(2w–1–1) = –22w–2 + 2w–1
    Up to 2w–1 bits
  Two’s complement max: x * y ≤ (–2w–1) 2 = 22w–2
    Up to 2w bits, but only for (TMinw)2
Maintaining Exact Results
  Would need to keep expanding word size with each product computed
  Done in software by “arbitrary precision” arithmetic packages

## Slide 18: Unsigned Multiplication in C
Standard Multiplication Function
  Ignores high order w bits
Implements Modular Arithmetic
  UMultw(u , v) = (u · v ) mod 2w
• • •
• • •
u
v
*
• • •
u · v
• • •
True Product: 2*w bits
Operands: w bits
Discard w bits: w bits
UMultw(u , v)
• • •

## Slide 19: Unsigned vs. Signed Multiplication
Unsigned Multiplication
  unsigned ux = (unsigned) x;
  unsigned uy = (unsigned) y;
  unsigned up = ux * uy
  Truncates product to w-bit number up = UMultw(ux, uy)
  Modular arithmetic: up = (ux  uy) mod 2w
Two’s Complement Multiplication
  int x, y;
  int p = x * y;
  Compute exact product of two w-bit numbers x, y
  Truncate result to w-bit number p = TMultw(x, y)
  Signed multiplication gives same bit-level result as unsigned
  up == (unsigned) p
Notes: One way to think of why signed multiplication gives the same bit-level result as unsigned multiplication in this case, i.e. up == (unsigned) p, is that multiplication can be broken down into a series of bit-shift-lefts and sums, both of which look identical in bit-level hardware whether signed or unsigned. Therefore, multiplication should also generate the same bit-level result.

## Slide 20: Power-of-2 Multiply with Shift
Examples
  u << 3 == u * 8
  u << 5 - u << 3 == u * 24
  Most machines shift and add much faster than multiply
    Compiler generates this code automatically
0
0
1
0
0
0
•••
2k
*
•••
• • •
u
Operands: w bits
k
True Product: w+k bits
u · 2k
• • •
0
0
0
•••
Discard k bits: w bits
UMultw(u , 2k)
TMultw(u , 2k)
0
0
0
•••
•••
Operation
  u << k gives u * 2k
  Both signed and unsigned

## Slide 21: General Multiplication via Shifts and Adds
Any integer can be expressed as a sum of powers of 2
  Example: 37 = 32 + 4 + 1 = 25 + 22 + 20
  Example: 117 = 64 + 32 + 16 + 4 + 1 = 26 + 25 + 24 + 22 + 20
A product of two integers can therefore be expressed as an integer times a sum of powers of 2
  Example: 6*37 = 6*(25 + 22 + 20)
  = 6*25 + 6*22 + 6*20
  = 6 << 5 + 6 << 2 + 6
  = 000001102 << 5 + 000001102 << 2 + 000001102
  = 110000002 + 000110002 + 000001102
  = 110111102 = 22210

## Slide 22: Unsigned Power-of-2 Divide with Shift
Quotient of Unsigned by Power of 2
  u >> k gives  u / 2k   “floor” function or RoundDown
  Uses logical shift
0
0
1
0
0
0
•••
2k
/
•••
k
u
Operands:
•••
•••
Binary Point
u / 2k
Division:
•••
0
•••
•••
.
 u / 2k 
•••
Result:
0
•••
Notes: Floor(x) = largest integer not greater than x.
Note that the yellow “MS bits” region does not necessarily align up after shifting with the green shifting bit, which the picture could be misinterpreted to imply. For example, if k is large, then the yellow region will be small. After shifting (u/2^k), the yellow region will be far to the right, while the green shifting bit will be far to the left – the difference would then be clear. Similarly, if k is small, then the yellow region will be large. After shifting, the upper edge of the yellow blocks will be on the far left, whereas the position of the green shifting bit will be to the far right – again the difference would be clear.

## Slide 23: Signed Power-of-2 Divide with Shift
Quotient of Signed by Power of 2
  x >> k gives  x / 2k 
  Uses arithmetic shift
  Rounds wrong direction when x < 0
0
0
1
0
0
0
•••
2k
/
•••
k
x
Operands:
•••
•••
Binary Point
x / 2k
Division:
•••
0
•••
•••
.
RoundDown(x / 2k)
•••
Result:
0
•••
Need to add one!
Notes: We also need to not add one when the division is exact and there is no remainder to throw away to the right of the binary point.

## Slide 24: Correct Power-of-2 Divide
Quotient of Negative Number by Power of 2
  Want  x / 2k  (Round Toward 0)  “ceiling” function
  Compute as  (x+2k-1)/ 2k 
    Adding a pre-bias 2k - 1
    In C: (x + (1<<k)-1) >> k
    Biases dividend toward 0
Case 1: No rounding
Divisor:
0
0
1
0
0
0
•••
2k
/
•••
k
0
0
0
1
1
1
•••
+2k +–1
•••
    Biasing has no effect
Dividend:
x
1
•••
0
0
0
•••
1
1
•••
1
1
1
•••
1
 x / 2k 
1
•••
0
1
1
•••
.
Binary Point
1
1
1
1
•••
1
1
1
1
…
Notes: Ceiling(x) = smallest integer not less than x

## Slide 25: Correct Power-of-2 Divide (Cont.)
Case 2: Rounding
Divisor:
0
0
1
0
0
0
•••
2k
/
•••
    Biasing adds the desired 1 to final result
k
Dividend:
x
1
•••
•••
0
0
0
1
1
1
•••
+2k +–1
•••
1
1
•••
•••
Incremented by 1
1
 x / 2k 
1
•••
0
1
1
•••
.
Binary Point
1
•••
Incremented by 1
1
1
1
1

## Slide 26: In C, Signed 2k Division via >>
The default for >> is RoundDown() or the Floor function
  Either positive or negative
  Imprecision for RoundDown for negative #’s
To get RoundToZero() rounding in signed 2k Division, you have to implement the following C code:
  (x<0 ? x+(1<<k)-1 : x) >> k
  This is equivalent to:
  If (x<0) {
  quotient = (x+2k – 1) >> k /* pre-bias by 2k – 1 before
  right-shifting*/
  } else { /* x >= 0 */
  quotient = x >> k
  }

## Slide 27: No Shortcuts to General Integer Division
Example: 117/37
  = 117/(25 + 22 + 20) ≠ 117/25 + 117/22 + 117/20
  Cannot distribute the division, unlike the multiplication
  So we cannot easily use a sum of right shifts as a shortcut for general integer division
Special hardware circuits are designed to implement an integer division
  Access these integer division circuits by invoking the appropriate assembly language instruction, e.g. idivl

## Slide 28: Supplementary Slides

## Slide 29: Mathematical Properties
Modular Addition Forms an Abelian Group
  Closed under addition
    0  UAddw(u , v)  2w –1
  Commutative
    UAddw(u , v) = UAddw(v , u)
  Associative
    UAddw(t, UAddw(u , v)) = UAddw(UAddw(t, u ), v)
  0 is additive identity
    UAddw(u , 0) = u
  Every element has additive inverse
    Let UCompw (u ) = 2w – u
    UAddw(u , UCompw (u )) = 0

## Slide 30: Properties of Unsigned Arithmetic
Unsigned Multiplication with Addition Forms Commutative Ring
  Addition is commutative group
  Closed under multiplication
    0  UMultw(u , v)  2w –1
  Multiplication Commutative
    UMultw(u , v) = UMultw(v , u)
  Multiplication is Associative
    UMultw(t, UMultw(u , v)) = UMultw(UMultw(t, u ), v)
  1 is multiplicative identity
    UMultw(u , 1) = u
  Multiplication distributes over addtion
    UMultw(t, UAddw(u , v)) = UAddw(UMultw(t, u ), UMultw(t, v))

## Slide 31: Properties of Two’s Comp. Arithmetic
Isomorphic Algebras
  Unsigned multiplication and addition
    Truncating to w bits
  Two’s complement multiplication and addition
    Truncating to w bits
Both Form Rings
  Isomorphic to ring of integers mod 2w
Comparison to Integer Arithmetic
  Both are rings
  Integers obey ordering properties, e.g.,
    u > 0  u + v > v
    u > 0, v > 0  u · v > 0
  These properties are not obeyed by two’s comp. arithmetic
    TMax + 1 == TMin
    15213 * 30426 == -10030 (16-bit words)