## Slide 1: Chapter 3: Assembly Language Programming I
Topics
  Assembly Programmer’s Execution Model
  Accessing Information
    Registers
    Memory

## Slide 2: Chapter Mapping
Lines of
Source
code
Lines of
Assembly
code
Lines of
Binary
code &
data
10101010
00001010
01010111
Memory
11101110
00111011
10000111
10101010
add a,b
sub a,b
move a…
Chapter 3
Chapters 3, 4, 5 and 6
Chapter 2
Pre-processor
&
Compiler
Assembler
&
Linker
Operating
System

## Slide 3: Intel x86 Processors
Totally dominate PC computer market
Evolutionary design
  Backwards compatible up until 8086 16-bit CPU, introduced in 1978
  Then 80286, 80386, 80486, Pentium, …, Intel Core i7 – hence the name x86
  Added more features as time goes on
Complex instruction set computer (CISC)
  Many different instructions with many different formats
    But, only small subset encountered with Linux programs
  Hard to match performance of Reduced Instruction Set Computers (RISC)
  But, Intel has done just that!

## Slide 4: Assembly Language
Specific to a CPU
  We will be using x86 assembly language
  ARM processors will have a different assembly language, etc.
  32-bit processors will have different assembly language than 64-bit processors
Different styles for x86-64 assembly code
  We will be using gcc/GNU-style assembly language
  There is also the Intel style of assembly language
    Example: switches order of source and destination compared to gcc/GNU

## Slide 5: Assembly Programmer’s View
Programmer-Visible State
  EIP Program Counter
    Address of next instruction
  Register File
    Heavily used program data
  Condition Codes
    Store status information about most recent arithmetic operation
    Used for conditional branching
EIP
Registers
CPU
Memory
Object Code
Program Data
OS Data
Addresses
Data
Instructions
Call
Stack
Condition
Codes
  Memory
    Byte addressable array
    Code, user data, (some) OS data
    Includes call stack used to support procedures
ALU

## Slide 6: Turning C into Object Code
text
C program (p1.c p2.c)
text
Compiler (gcc -Og -S)
Asm program (p1.s p2.s)
binary
Assembler (gcc or as)
Object program (p1.o p2.o)
binary
Linker (gcc or ld)
Executable program (p)
Static libraries (.a)
  Code in files p1.c p2.c
  Compile with command: gcc -Og p1.c p2.c -o p
    Use basic optimizations (-Og) [New to recent versions of gcc]
    Put resulting binary in file p

## Slide 7: Compiling Into Assembly
C Code (sum.c)
long plus(long x, long y);
void sumstore(long x, long y,
long *dest)
{
long t = plus(x, y);
*dest = t;
}
Generated x86-64 Assembly
sumstore:
pushq %rbx
movq %rdx, %rbx
call plus
movq %rax, (%rbx)
popq %rbx
ret
Obtain (on VM) with command
  gcc –Og –S sum.c
Produces file sum.s
Note how assembly maps to C code
Note: May get very different results on other machines, even other Linux machines, due to different versions of gcc and different compiler settings

## Slide 8: Object Code sum.o
Code for sumstore
0x0400595:
0x53
0x48
0x89
0xd3
0xe8
0xf2
0xff
0xff
0xff
0x48
0x89
0x03
0x5b
0xc3
Total of 14 bytes
Each instruction 1, 3, or 5 bytes
Starts at address 0x0400595

## Slide 9: Disassembling Object Code
Disassembled
Disassembler
  objdump –d sum
  Useful tool for examining object code
  Analyzes bit pattern of series of instructions
  Produces approximate rendition of assembly code
  Can be run on either a.out (complete executable) or .o file
0000000000400595 <sumstore>:
400595: 53 push %rbx
400596: 48 89 d3 mov %rdx,%rbx
400599: e8 f2 ff ff ff callq 400590 <plus>
40059e: 48 89 03 mov %rax,(%rbx)
4005a1: 5b pop %rbx
4005a2: c3 retq

## Slide 10: Alternate Disassembly
Disassembled
Dump of assembler code for function sumstore:
0x0000000000400595 <+0>: push %rbx
0x0000000000400596 <+1>: mov %rdx,%rbx
0x0000000000400599 <+4>: callq 0x400590 <plus>
0x000000000040059e <+9>: mov %rax,(%rbx)
0x00000000004005a1 <+12>:pop %rbx
0x00000000004005a2 <+13>:retq
Within gdb Debugger
  gdb sum
  disassemble sumstore
  Disassemble procedure
  x/14xb sumstore
  Examine the 14 bytes starting at sumstore
Object
0x0400595:
0x53
0x48
0x89
0xd3
0xe8
0xf2
0xff
0xff
0xff
0x48
0x89
0x03
0x5b
0xc3

## Slide 11: What Can be Disassembled?
Anything that can be interpreted as executable code
Disassembler examines bytes and reconstructs assembly source
% objdump -d WINWORD.EXE
WINWORD.EXE: file format pei-i386
No symbols in "WINWORD.EXE".
Disassembly of section .text:
30001000 <.text>:
30001000: 55 push %ebp
30001001: 8b ec mov %esp,%ebp
30001003: 6a ff push $0xffffffff
30001005: 68 90 10 00 30 push $0x30001090
3000100a: 68 91 dc 4c 30 push $0x304cdc91
Reverse engineering forbidden by
Microsoft End User License Agreement

## Slide 12: x86-64 Integer Registers
%rsp
  Can reference low-order 4 bytes (also low-order 1 & 2 bytes)
%eax
%ebx
%ecx
%edx
%esi
%edi
%esp
%ebp
%r8d
%r9d
%r10d
%r11d
%r12d
%r13d
%r14d
%r15d
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp

## Slide 13: Some History: IA32 registers
%eax
%ecx
%edx
%ebx
%esi
%edi
%esp
%ebp
%ax
%cx
%dx
%bx
%si
%di
%sp
%bp
%ah
%ch
%dh
%bh
%al
%cl
%dl
%bl
16-bit virtual registers
(backwards compatibility)
general purpose
accumulate
counter
data
base
source
index
destination
index
stack
pointer
base
pointer
Origin
(mostly obsolete)

## Slide 14: Moving Data
Moving Data
  movq Source, Dest
  Move 8-byte (“quad”) word
  Lots of these in typical code
Operand Types
  Register: One of 16 integer registers
    Example: %rax, %r13
    But %rsp reserved for special use
    Others have special uses for particular instructions
%rax
%rcx
%rdx
%rbx
%rsi
%rdi
%rsp
%rbp
%rN

## Slide 15: Moving Data
Moving Data
  movq Source, Dest
Operand Types
  Immediate: Constant integer data
    Example: $0x400, $-533
    Like C constant, but prefixed with ‘$’
    Encoded with 1, 2, or 4 bytes
  Memory: 8 consecutive bytes of memory at address given by register
    Simplest example: (%rax)
    Various other “address modes”
%rax
%rcx
%rdx
%rbx
%rsi
%rdi
%rsp
%rbp
%rN

## Slide 16: Representing Instructions
For historical reasons (16-bit processors), Intel terminology considers a “word” to be 16 bits long
  ‘movw %ax, %dx’, where the ‘w’ in movw implies a 16 bit quantity is about to be moved
  ‘movl %eax, %edx’, the ‘l’ in movl implies a “long” 32-bit quantity is about to be moved.
  See text for more mov instructions: movb, movw, movl, movsbw, movsbl, movswl, movzbw, movzbl, movzwl
Does the width of a C ‘long’ int == an x86 assembly language ‘long’ word?
  Yes, they’re both 32-bits or 4 bytes on a 32-bit x86 machine
  No, a C ‘long’ is 64-bits on a 64-bit x86 machine, while an x86 assembly language ‘long’ is still 32-bits wide
    i.e. a movl on a 64-bit machine is still going to move a 32-bit quantity

## Slide 17: Moving Data Examples
Examples
  Moving the value in one register to another
  Moving a value at a memory location to a register
  Moving a register value to a memory location
64 bits wide
Memory
1.
2.
3.
CPU registers
%rax
%rcx
%rdx
%rbx
%rsi
%rdi
%rsp
%rbp
%rN

## Slide 18: movq Operand Combinations
movq
Imm
Reg
Mem
Reg
Mem
Reg
Mem
Reg
Source
Dest
C Analog
movq $0x4,%rax
temp = 0x4;
movq $-147,(%rax)
*p = -147;
movq %rax,%rdx
temp2 = temp1;
movq %rax,(%rdx)
*p = temp;
movq (%rax),%rdx
temp = *p;
Src,Dest
  Cannot do memory-memory transfers with single instruction
    i.e. can’t do: movq (%rax), (%rdx)

## Slide 19: Simple Addressing Modes
Normal (R) Mem[Reg[R]]
  Register R specifies memory address
  movq (%rcx),%rax
Displacement D(R) Mem[Reg[R]+D]
  Register R specifies start of memory region
  Constant displacement D specifies offset
  movq 8(%rbp),%rdx
Go to memory address %rbp+8
and fetch the data located there

## Slide 20: Supplementary Slides