## Slide 1: Chapter 3: Function calls and the Stack pointer
Topics
  IA64 stack discipline
  %rsp
  Push, pop
  Call, ret

## Slide 2: Announcements
Data Lab grading this week
  Sign up for 12-minute slots, come prepared and don’t forget!
Next Assembly Quiz on moodle, due Mon Feb 13 by noon
Bomb Lab #2 released, due Friday Feb 24 by 11:55 pm
  Fixed glitch in bomb server preventing bomb downloads
  Can form teams of two
  Extra credit secret bomb
Read Chapter 3.1-3.12 (except 3.11) and do practice problems

## Slide 3: Sparse Switch Example
  Not practical to use jump table
    Would require 10000 entries!
    Most of entries in jump table are the same default
  Obvious translation into if-then-else would have maximum of 9 tests in the worst case
    Can we do better?
    Yes, use a tree-based approach – logarithmic in # tests (e.g. 4)
/* Return x/1111 if x is multiple
&& <= 9999. -1 otherwise */
int div1111(int x)
{
switch(x) {
case 0: return 0;
case 1111: return 1;
case 2222: return 2;
case 3333: return 3;
case 4444: return 4;
case 5555: return 5;
case 6666: return 6;
case 7777: return 7;
case 8888: return 8;
case 9999: return 9;
default: return -1;
}
}

## Slide 4: Chapter 3.7 Procedures and the Stack Pointer

## Slide 5: Procedures/Function Calls
Procedures/functions allow logical grouping of code
  Enable reuse of code, which can be called from different places in the program
Memory
Computes
factorial
Computes
polynomial
Code
Data
factorial(10);
polynomial(…);
factorial(int n) {
…
…
}
polynomial(…) {
…
…
}
factorial(7);

## Slide 6: Motivation for a Call Stack (1)
Imagine the world of early programming
  No functions
  No stack pointers or stacks. No frame pointers or frames
Memory
Computes
factorial
Computes
polynomial
Code
Data

## Slide 7: Motivation for a Call Stack (2)
Suppose 2 parts of code want to execute the same computation
  Repeating the computational code is inefficient
  Maintaining multiple copies of same computation is inconvenient
Computes
factorial
Computes
factorial
Computes
polynomial

## Slide 8: Motivation for a Call Stack (3)
Instead, write the common code once and jump to it from different locations
  Problem #1: How do you jump back?
Computes
factorial
Computes
polynomial
0x20
0x44
0x68
jmp 0x68
jmp 0x68
Jump back where?
  Must remember the address where you were calling the common code from
  Could allocate some memory to store the return address for this factorial code

## Slide 9: Motivation for a Call Stack (4)
Before each jump to the common code, store return address in special memory location
Computes
factorial
Computes
polynomial
0x20
0x44
0x68
jmp 0x68
jmp 0x68
Store the return
address of the next
instruction after
the jump in a special
memory location, e.g.
0xf0 in this example
for factorial code
(location not shown)
movq $0x28, (0xf0)
movq $0x4c, (0xf0)
jmp *(0xf0)
  Problem: can’t share 1 mem location for all return addresses
    1 set of common code may call another set
    Instead, would need 1 return address location for each set of common code
Problem:
Recursion?
  Jump back using this special location
Notes: Example: polynomial code may want to call factorial code.
Note: each common code fragment would need to be separately programmed to consult a different memory location to find its return address.
A key problem of having one memory location to store the return address for each function is this won’t work for recursive calls. In that case, you need to have a memory location to store the return address for each *invocation* of a function.
Another problem is that you can’t have two calls concurrently inside the same function, as would occur in a multi-threaded program.
A third problem is that if the function is never called, then you’ve wasted space allocating memory for storing a return address.

## Slide 10: Motivation for a Call Stack (5)
Problem #2: How to pass parameters to common code?
  Example: from the 1st jump point, may want to calculate 10!, while 2nd jump point may want to calculate 7!
  Again, could allocate special memory to store parameters before jumping
Computes
factorial
Computes
polynomial
0x20
0x44
0x68
jmp 0x68
jmp 0x68
Store parameters
before jump
movq $10, (0xf8)
movq $7, (0xf8)
movq (0xf8), %rbx
Retrieve parameters
after jump
  The called common code is programmed to look in this special memory location to retrieve parameters
Problem:
Recur-
sion?
Problem:
Waste
Memory
Notes: A problem again is inefficiency - if the function is never called, then the space allocated for saving parameters is wasted memory.
The problem again is also recursion.

## Slide 11: Motivation for a Call Stack (6)
Problem #3: Wasting memory
  the common code may never be called, wasting allocated memory for parameters and return addresses
Problem #4: Wasting memory II
  the common code may allocate local variables only used within the common code, yet the common code may never be called, wasting memory

## Slide 12: Motivation for a Call Stack (7)
Design goals: want a solution to support functions that:
  Automatically stores the return address before a function is called, and retrieves that return address when exiting a function
  Allows storage of parameters before a function is called, and parameter retrieval within the function
  Is memory-efficient for return addresses, parameters, and local variables
  Each instance of a function should have its own unique set of {return address, parameters, and local variables}, to support recursion (and multi-threading)

## Slide 13: Solution: a Call Stack
Supports function calls by storing the return address, parameters, and local variables on a stack
  Allocate a special reusable region of memory for the stack
  Create a special CPU register %rsp that the stores the location of the top of the stack, i.e. the stack pointer
  Create a CPU instruction call that before jumping to a function stores (pushes) the return address on the stack
  Create a CPU instruction ret that jumps to the return address upon exiting from the function, popping the address from the stack
Code
Data
Memory
Stack
Space
0x0000
0xMAX
initial %rsp

## Slide 14: Solution: a Call Stack (2)
On each function call, and before executing the body of the function,
  Push parameters onto the stack
  Push return address onto the stack
  Push/allocate local variables on the stack
Code
Data
Memory
Stack
Space
0x0000
0xMAX
new
%rsp
params
return addr
local
variables
Stack grows up/down
initial %rsp
  Must also save the old location of the stack pointer so it can be restored to its old value after exiting the function
  If a function f1 calls a function f2, then the stack grows down even more. If f2 calls a function f3, that grows the stack.
  As each function finishes/calls return, its local variables, return address, and parameters are popped off the stack (deallocated), shrinking the stack
Notes: As we’ll see later, usually there is also room made on the call stack for saved registers that are restored when the procedure exits.

## Slide 15: Solution: a Call Stack (3)
In this way, we satisfy the original design goals:
  Enables passing parameters to functions
  Automated support for storing the return address
  Memory-efficient storage that reuses memory and only allocates space for parameters, return addresses, and local variables if a function is called
  Supports recursion – each instance/call of a function has its own stack frames to store its own return address, parameters, and local variables
Code
Data
Memory
Stack
Space
0x0000
0xMAX
new
%rsp
params
return addr
local
variables
Stack grows up/down

## Slide 16: Layout of a Program in Memory
Code, data, heap and stack segments
  Data stores global variables
Stack grows down from high memory by convention on x86-64
  Stores local variables
  Supports function calls
Heap grows up from low memory by convention
  Supports dynamic run-time memory allocation like malloc()
MAX
Notes: This is actually virtual memory, not physical memory.

## Slide 17: Pushing parameters onto the stack
In X86-64:
  The first 6 arguments are passed into a procedure using 6 CPU registers:
Argument # | 1 | 2 | 3 | 4 | 5 | 6
register | %rdi | %rsi | %rdx | %rcx | %r8 | %r9
  The remaining 7+ arguments if any are passed by pushing onto the call stack
  If an argument is less than 8 bytes wide, then the appropriate lower order bytes of the above registers are used
In 32-bit X86 systems:
  All parameters are passed into a procedure by pushing them onto the stack
  This is slower than passing by register, because memory accesses to the stack are slower than CPU registers
Notes: See Figure 3.28 p. 245.

## Slide 18: x86-64 Stack
Region of memory managed with stack discipline
Grows toward lower addresses
Register %rsp contains lowest stack address
  address of “top” element
Stack Pointer: %rsp
Stack Grows
Down
Increasing
Addresses
Stack “Top”
Stack “Bottom”

## Slide 19: x86-64 Stack: Push
pushq Src
  Fetch operand at Src
  Decrement %rsp by 8
  Write operand at address given by %rsp
-8
Stack Grows
Down
Increasing
Addresses
Stack “Bottom”
Stack Pointer: %rsp
Stack “Top”

## Slide 20: x86-64 Stack: Pop
Stack Pointer: %rsp
Stack Grows
Down
Increasing
Addresses
Stack “Top”
Stack “Bottom”
+8
popq Dest
  Read value at address given by %rsp
  Increment %rsp by 8
  Store value at Dest (must be register)

## Slide 21: Code Examples
long mult2
(long a, long b)
{
long s = a * b;
return s;
}
void multstore
(long x, long y, long *dest) {
long t = mult2(x, y);
*dest = t;
}
0000000000400550 <mult2>:
400550: mov %rdi,%rax # a
400553: imul %rsi,%rax # a * b
400557: retq # Return
0000000000400540 <multstore>:
400540: push %rbx # Save %rbx
400541: mov %rdx,%rbx # Save dest
400544: callq 400550 <mult2> # mult2(x,y)
400549: mov %rax,(%rbx) # Save at dest
40054c: pop %rbx # Restore %rbx
40054d: retq # Return

## Slide 22: Procedure Control Flow
Use stack to support procedure call and return
Procedure call: call label
  Push return address on stack
  Jump to label
Return address:
  Address of the next instruction right after call
  Example from disassembly
Procedure return: ret
  Pop address from stack
  Jump to address

## Slide 23: Control Flow Example #1
0000000000400550 <mult2>:
400550: mov %rdi,%rax
•
•
400557: retq
0000000000400540 <multstore>:
•
•
400544: callq 400550 <mult2>
400549: mov %rax,(%rbx)
•
•
0x400544
0x120
•
•
•
%rsp
0x120
0x128
0x130
%rip

## Slide 24: Control Flow Example #2
0000000000400550 <mult2>:
400550: mov %rdi,%rax
•
•
400557: retq
0000000000400540 <multstore>:
•
•
400544: callq 400550 <mult2>
400549: mov %rax,(%rbx)
•
•
0x400550
0x118
0x400549
•
•
•
%rsp
0x120
0x128
0x130
0x118
%rip

## Slide 25: Control Flow Example #3
0000000000400550 <mult2>:
400550: mov %rdi,%rax
•
•
400557: retq
0000000000400540 <multstore>:
•
•
400544: callq 400550 <mult2>
400549: mov %rax,(%rbx)
•
•
0x400557
0x118
0x400549
•
•
•
%rsp
0x120
0x128
0x130
0x118
%rip

## Slide 26: Control Flow Example #4
0000000000400550 <mult2>:
400550: mov %rdi,%rax
•
•
400557: retq
0000000000400540 <multstore>:
•
•
400544: callq 400550 <mult2>
400549: mov %rax,(%rbx)
•
•
0x400549
0x120
•
•
•
%rsp
0x120
0x128
0x130
%rip

## Slide 27: Procedure Data Flow
Registers
First 6 arguments
Return value
Stack
Only allocate stack space when needed
%rdi
%rsi
%rdx
%rcx
%r8
%r9
%rax
Arg 7
• • •
Arg 8
Arg n
• • •

## Slide 28: Data Flow Examples
long mult2
(long a, long b)
{
long s = a * b;
return s;
}
void multstore
(long x, long y, long *dest) {
long t = mult2(x, y);
*dest = t;
}
0000000000400550 <mult2>:
# a in %rdi, b in %rsi
400550: mov %rdi,%rax # a
400553: imul %rsi,%rax # a * b
# s in %rax
400557: retq # Return
0000000000400540 <multstore>:
# x in %rdi, y in %rsi, dest in %rdx
• • •
400541: mov %rdx,%rbx # Save dest
400544: callq 400550 <mult2> # mult2(x,y)
# t in %rax
400549: mov %rax,(%rbx) # Save at dest
• • •

## Slide 29: Supplementary Slides

## Slide 30: Stack Operation Examples
%esp
%eax
%edx
213
%esp
%eax
%edx
0x108
0x10c
0x110
0x104
0x108
555
213
123
0x108
0x10c
0x110
555
213
123
0x108
0x104
pushl %eax
popl %edx
%esp
%eax
%edx
0x104
555
0x108
0x10c
0x110
213
123
0x104
213
stack
CPU registers
213
0x108

## Slide 31: Procedure Control Flow
  Use stack to support procedure call and return
Procedure call:
  call label Push return address on stack; Jump to label
  Example: if my function name is swap_numbers, then
    call swap_numbers
Return address value
  Address of instruction beyond call
  Example from disassembly
  804854e: e8 3d 06 00 00 call 8048b90 <main>
  8048553: 50 pushl %eax
    Return address = 0x8048553
Procedure return:
  ret Pop address from stack; Jump to address

## Slide 32: Procedure Call Example
%esp
%eip
0x804854e
0x8048553
%esp
%eip
0x804854e
0x108
0x108
0x10c
0x110
0x104
123
0x108
0x10c
0x110
123
0x108
call 8048b90
  804854e: e8 3d 06 00 00 call 8048b90 <main>
  8048553: 50 pushl %eax
0x8048b90
0x104
%eip is program counter
stack
CPU registers

## Slide 33: Procedure Return Example
%esp
%eip
0x104
0x8048591
0x104
0x108
0x10c
0x110
0x8048553
123
ret
  8048591: c3 ret
%eip is program counter
%esp
%eip
0x8048591
0x104
0x108
0x10c
0x110
123
0x8048553
0x108
0x8048553

## Slide 34: IA32/Linux Stack Frame
Caller Stack Frame
  Push parameters for function about to call
    “Argument build”
    Last argument pushed first, … first argument is pushed last – see p.220 of textbook
  Push return address
    Pushed by call instruction
Current Callee Stack Frame
  Push (save) old frame pointer
  Saved register context
  Allocate space for local variables
  More argument building as needed
Stack Pointer
(%esp)
Frame Pointer
(%ebp)
Return Addr
Saved
Registers
+
Local
Variables
Argument
Build
Old %ebp
Arguments
Caller
Frame
Current
Callee
Frame
Notes: The last argument is pushed first, and the first argument is pushed last - see p. 220 of the textbook.

## Slide 35: ipwr Computation
/* Compute x raised to nonnegative power p */
int ipwr_for_fast(int x, unsigned p) {
int result;
for (result = 1; p != 0; p = p>>1) {
if (p & 0x1)
result *= x;
x = x*x;
}
return result;
}

## Slide 36: Summarizing
C Control
  if-then-else
  do-while
  while
  switch
Assembler Control
  jump
  Conditional jump
Compiler
  Must generate assembly code to implement more complex control
Standard Techniques
  All loops converted to do-while form
  Large switch statements use jump tables
Conditions in CISC
  CISC machines generally have condition code registers
Conditions in RISC
  Use general registers to store condition information
  Special comparison instructions
  E.g., on Alpha:
  cmple $16,1,$1
    Sets register $1 to 1 when Register $16 <= 1